http://www.drakacomteq.us/index.cfm

Optical Fiber Types
» Optical Fiber | Singlemode
» Optical Fiber | Multimode

OPTICAL FIBERS | Singlemode
As the second largest supplier of optical fiber worldwide, Draka provides high performance fiber that fits your real world applications - with more than 20 million miles of fiber deployed in North America alone.

Commonly used for long-distance links, singlemode optical fiber networks support higher transmission rates, provide minimal signal attenuation and travel longer distances than multimode fiber before needing a repeater. This is why most networks more than 1 kilometer (3280 feet) use primarily singlemode fibers. Singlemode fibers from Draka have an extremely high transmission capacity in combination with low optical losses. These properties make our singlemode fiber ideal for optical systems operating at high transmission speeds over long distances. They are also the medium of choice for upgrading traditional copper telephone lines to the needs of the 21st century. Their flexibility makes these fiber cables easy to install - reducing cost, bend-induced losses, footprint size, and complexity.

| ESMF, BendBright, TeraLight |
| --- |
|  | Product Snapshot Applications Extended Spans & High Data Rates Used in Telecom, CATV, FttX, Long-Haul Transmission Typically includes SONET, SDH, DWDM, ATM, Ethernet, IP, Analog Video & others Benefits Low Attenuation / DWDM Spectrum / Lifetime Reliability / ColorLock® Coating Fiber Types ESMF: Full Spectrum 1260-1625nm (G.652D) BendBright: ESMF with up to 10x Bend Performance (G.652D) BendBrightXS: ESMF with 10-100x Bend Performance (G.652D, G.657) Performance ITU-T, IEC 60793-2-50, ANSI/ICEA, RDUP, Telcordia GR-20-CORE Ordering Information Application Fiber Code Spec (ITU) ESMF Enhanced Singlemode Metro ES G.652D BendBright Metro, Access BB G.652D BendBrightXS Metro, Access BX G.652D, G.657 |

http://www.drakacomteq.us/ofsinglemode.cfm

OPTICAL FIBERS | Multimode
As the largest supplier of multimode fiber worldwide, Draka provides high performance fiber that fits your real world applications - including the latest MaxCap family of laser-optimized OM-3 fibers to support 10 Gb Ethernet up to 550 meters (1,800').

| MaxCap™, HiCap™, Standard Multimode |
| --- |
|  | Product Snapshot Applications Building, Campus, Data Center & Local Area Transmission Typically includes Gigabit Ethernet (10 GbE, 1 GbE), ATM, Fibre Channel, FDDI, Token Ring & others Benefits Compatible with economical LEDs and VCSELs / Coupling Efficiency / High Bandwidth / Laser Optimized / Precision PCVD Process Fiber Types MaxCap: Maximum Bandwidth / 10 GbE optimized / 50um core HiCap: High Bandwidth / 1 GbE optimized / 50 & 62.5um core Standard: Legacy Bandwidth / Up to 1 GbE distance-limited / 50 & 62.5um core Performance IEC 60793-2-10, ISO/IEC 11801, TIA-492A Ordering Information Core Size Fiber Code Spec (ISO/IEC) MaxCap 550 (10 GbE / 550m) 50um 55 OM-3+ / A1a.2 MaxCap 300 (10 GbE / 300m) 50um 53 OM-3+ / A1a.2 MaxCap 150 (10 GbE / 150m) 50um 51 OM-3 / A1a.2 HiCap (1 GbE optimized) 50um 5H OM-2+ / A1a.1 HiCap (1 GbE optimized) 62.5um 6H OM-1+ / A1b Legacy 50um (std Graded Index) 50um 5S OM-2 / A1a.1 Legacy 62.5um (std Graded Index) 62.5um 6S OM-1 / A1b |

http://www.drakacomteq.us/ofmultimode.cfm

CATV

CATV MSOs (Multi System Operators) and other broadcast/video operators are using fiber to help grow and extend broadband services - thorugh more high-definition channels, higher broadband access speeds, and bundled "triple play" services. The Hybrid Fiber Coax (HFC) infrastructure continues to evolve to ever deeper Fiber-to-the-Node and Fiber-to-the-Passive network, supporting cost-effective migration and growth. Fiber also supports extending new services to residential and business customers. From the Head End to the home, the impact of deep fiber infrastructure is clear - reducing long-term operational expense, and providing a platform for future growth and scalability.

| Network Segment |
| --- |
| Network Segment | Cabling Solutions | Connectivity Solutions | Optical Fiber Solutions |
| Head End | LANnet » Indoor-Outdoor » ezDISTRIBUTION | LANnet » ezPATCH-SPLICE | » BendBright » BendBrightXS |
| Trunk | TERRAnet » ezPREP Loose Tube | » ezCLOSURE | » ESMF Singlemode |
| Feeder | TERRAnet » ezPREP Loose Tube » Central loose Tube | HOMEnet » ezCABINET » ezCLOSURE | » ESMF Singlemode » Bendbright |
| Node/Drop | HOMEnet » Node Cable » ezDROP Flat Preconnectorized Ribbon |  | » BendBright » BendBrightXS |

http://www.drakacomteq.us/catv.cfm

TERRAnet | Multi-Purpose Cabling

| Product | Data Sheets | Procedures | Background |
| --- | --- | --- | --- |
| ezPREP Loose Tube | Loose Tube (2 to 432f) Central Loose Tube (2 to 12f) Loose Tube ColdTemp (2 to 288f) Loose Tube ¦ Gel-Free (2 to 288f) Indoor-Outdoor (2 to 288f) | ezPREP Loose Tube ¦ Preparation & Handling | Summary White Paper |
| ezRIBBON | Central Tube Ribbon (12 to 432f) Loose Tube Ribbon (288 to 864f) | Central Tube Ribbon Preparation & Handling Loose Tube Ribbon Preparation & Handling Splittable Ribbon Access Ribbon Matrix Peel Kit | Summary |
| ezUNITUBE | Central Tube (2 to 96f) |  | Summary |
| ezTOOLS | Buffer Tube Access Tool Ribbon Tube Access Tool Cable Jacket Slitter Tool |  | Summary |

Back to Top

http://www.drakacomteq.us/resource.cfm#Terranet

HOMEnet | FttX Cabling

| Product | Data Sheets | Procedures | Background |
| --- | --- | --- | --- |
| ezDROP | Flat Drop (1 to 12f) Figure 8 Drop (2 to 6f) Ribbon Drop (4 or 6f) Preconnectorized Drop (1f) |  | Summary |
| ezCLOSURE | 450 Gel Sealed A Size ¦ 96 splices C Size ¦ 288 splices 400 Heat Sealed A Size ¦ 96 splices C Size ¦ 288 splices 400 OPGW Closure | 450 Gel Sealed A Size ¦ 96 splices B Size ¦ 144 splices D Size ¦ 768 splices MultiDrop Kit Ground Wire 400 Heat Sealed A Size ¦ 96 splices A8, B8 ¦ Drop Closure A8 ¦ Round Seal B Size ¦ 144 splices D Size ¦ 768 splices | Summary |
| ezCABINET | Splitter Cabinet Splitter Modules | Splitter Cabinet Splitter Modules Cross Connect Kit Pad Mount Frame Template ¦ 288f Pad Template ¦ 576f Pad Pole Mount Bracket Panel Replacement | Summary |
| ezTAP | Fiber Drop Enclosure Fiber Drop Terminal | Fiber Drop Terminal Aerial Bracket Pole Bracket | Summary |

Back to Top

http://www.drakacomteq.us/resource.cfm#Terranet

AEROnet | Aerial Self-Support Cabling

| Product | Data Sheets | Procedures | Background |
| --- | --- | --- | --- |
| ezSPAN ADSS | ADSS ¦ Short Span ADSS ¦ Long Span |  | Summary ADSS Worksheet |
| ezPREP Loose Tube Figure 8 | Figure 8 Loose Tube |  | Summary |
| ezOPGW | OPGW ¦ Central Tube OPGW ¦ Stranded Tube |  | Summary |

Back to Top

http://www.drakacomteq.us/resource.cfm#Terranet

OPTICAL FIBER

| Product | Data Sheets | Procedures | Background |
| --- | --- | --- | --- |
| Singlemode Fiber | ESMF (G.652D) BendBright (G.652D+) BendBrightXS (G.652D+, G.657A, G.657B) TeraLight (G.655, G.656) |  | Summary |
| Multimode Fiber | MaxCap (OM-3) 550 ¦ 300 ¦ 150 HiCap (OM-2+) HiCap XS (OM-2+) 50um Multimode (OM-2) 62.5um Multimode (OM-1) |  |  |

http://www.drakacomteq.us/resource.cfm#Terranet